## Slide 1: FINISHES
Everything you need to know to get started in Woodturning
THIS IS STILL JUST ONE OPINION. ALTHOUGH, I DO KNOW SOMETHING ABOUT THE CHEMISTRY OF FINISHES

## Slide 2: FINISHES FOR THE WOODTURNER
THE ONLY IMPORTANT QUESTION ABOUT FINISHING WOOD IS
“WHAT DO YOU LIKE?”
THIS IS TRUE FOR FLATWORK OR TURNED PROJECTS
There are many choices addressing the nature of the piece, eventual use, type of wood, personal preference

## Slide 3: FINISHES FOR THE WOODTURNER
The first step in finishing any wood project is preparing the surface to receive the top-coat (FILM) finish
NO FINISH IS ANY BETTER THAN THE SURFACE TO WHICH IT IS APPLIED
The surface is improved by
1)better cuts, 2)sharper tools, and 3)sanding
Sanding usually goes up through 400 to 600 grit
Exotic woods can easily be sanded through 2000 grit

## Slide 4: FINISHES FOR THE WOODTURNER
        FILM FINISHES
        The same products used in flatwork are available to the woodturner
        Urethanes, Lacquer, Shellac, Stains and dyes
        Most of you have used these finishes and the rules are not much different for lathe projects
        Less common in flatwork are Oil and Wax
            Important for food-use items

## Slide 5: FINISHES FOR THE WOODTURNER
                A major difference between flatwork and turning is that the lathe is a source of energy for drying and setting finishes as well as sanding
                FRICTION POLISHING allows finishes to be dried quickly- easier to build a finish on the lathe
                FRENCH POLISH is the flatwork analog
                In this case heat and speed are your friends
Notes: THE LATHE SUYPPLIES A SOURCE OF ENERGY TO DRIVE SETTING THE FINISH

## Slide 6: FINISHES FOR THE WOODTURNER
                Choice of finish depends on the final use of the project, i.e., items for food use
                Most finishes are food safe after drying
                It is important to know what is in the finish
                Ornamental projects can be finished with almost any product
                Drying agents are not safe for food-use projects because they do not evaporate-they stay on the surface-in the finish layer

## Slide 7: FINISHES FOR THE WOODTURNER
                DRYING OILS
                LINSEED, TUNG, WALNUT, POPPY SEED, and PERILLA OIL ARE THE NATURAL DRYING OILS
                Exposure to oxygen (also heat and light) cause these oils high in polyunsaturated fats to chemically bond to each other.
                Alkyd and other resins have replaced them in paints
Notes: THE TERM DRYING IS OFTEN THROWN AROUND IN DISCUSSIONS OF FINISHING. We should talk about drying for a minute.
Here, drying is not like water drying on a surface….Not Evaporation.
When Paint dries, liquids in the paint are converted to solids but chemical crosslinking.
The Natural drying oils can do that without additional chemicals

## Slide 8: FINISHES FOR THE WOODTURNER
DRYING AGENTS CAUSE OILS THAT ARE NOT NATURAL DRYING OILS TO HARDEN
“Japan Dryer” is a generic name for many drying agents. Japanese lacquer work is the oldest know use of drying agents-Urushiol
Common DRYING AGENTS are usually metal ions (Lead, Cadmium, Cobalt, Arsenic, Chromium, Zirconium) but organic drying agents are also used (Naptha derivatives, Methyl Ethyl Ketone derivatives)
Notes: URUSHIOL-MADE FROM WATER EXTRACT OF POISON IVY
DIHYDROJURUSHINOL
Lead has disappeared as a drying agent but that is what it did in lead based paint

## Slide 9: Applying an oil/wax friction polish
FOR FOOD-USE PIECES,
I PREFER A FRICTION
POLISHED OIL/WAX FINISH

## Slide 10: FINISHES FOR THE WOODTURNER
WHAT IS NOT A GOOD WOOD FINISH?
Mineral oil: A piece treated with mineral oil needs to be redressed every 30 days because it evaporates, exposing the open wood grain.
Beeswax: Exposure to air causes beeswax to begin to break down, producing white particles
Notes: WE CAN GO THROUGH THE STORY OF HOW AND WHY THE BUTCHERS BLOCK BROUGHT MINERAL OIL TO COMMON USE IF ANYONE IS INTERESTED

## Slide 11: FINISHES FOR THE WOODTURNER
The good news is that most beeswax sold in not pure beeswax. Mixture with other waxes (about 25-30%v/v) prevents this degradation process.
Notes: BEESWAX WEARS AWAY QUICKLY SO YOU WIND UP WITH MOSTLY THAT MIXED IN WAX ON THE SURFACE

## Slide 12: FINISHES FOR THE WOODTURNER
WHAT DO YOU LIKE?